ECE347

Lab3

(Amplifier Frequency Rersponse II)

Introduction:

The objective is to obtain the common emitter amplifier high frequency response, draw the bode plots.

Procedure:

Implement the following common emitter amplifier. Use a voltage divider in the front to get the small signal. Then, measure the gain (Vout/Vin) for the frequencies in the table.

| Frequency (Hz) | Gain (Vout/Vin) |
| --- | --- |
| 1k |  |  |
| 10k |  |  |
| 20k |  |  |
| 30k |  |  |
| 50k |  |  |
| 70k |  |  |
| 100k |  |  |
| 150k |  |  |
| 200k |  |  |
| 500k |  |  |
| 700k |  |  |
| 1M |  |  |
| 2M |  |  |

Conclusion:

From your measurements, find the -3dB frequencies, and draw the bode plot for the amplitude gain only. Evaluate Cje and Cjc. What is the difference between the two circuits ?